## Slide 1
DoseRAD2026 Photon Task 1: Baseline Update
Local project status for collaborator discussion | July 10, 2026
Goal: predict per-beam/control-point 3D dose from CT and beam geometry.
Input
CT + Bx/CPy parameters
Model
Geometry-conditioned 3D U-Net
Output
Dose_Bx_CPy.mha
Current status: baseline pipeline is complete and has produced first local validation results. Performance is still weak; the next phase is model improvement.

## Slide 2
Data And Preprocessing
What is already prepared locally
• Photon training dataset is downloaded locally.
• Case-level split is complete: 60 train cases / 15 validation cases.
• Preprocessing supports CT HU normalization.
• Optional HU-to-density conversion is implemented.
• Dose masks and dose statistics are available for support-region evaluation.
Data split
CT / density preprocessing
64 x 64 x 64 training crop
Dose and mask loading
Split file: splits/photon_case_split.csv

## Slide 3
Baseline Model
Geometry-conditioned 3D U-Net
CT volume
1-channel 3D image
Condition vector
beam, CP, gantry,
isocenter, MLC
FiLM-conditioned
3D U-Net
Predicted dose
Dose_Bx_CPy.mha
• Energy spectrum is optional for ablation, but current main baseline is no-energy.
• Model output was changed from ReLU to linear; exported dose is clamped to non-negative.

## Slide 4
Current Baseline Experiment
First reportable local run
Experiment
Name: baseline_hu_no_energy_v2_linear
Input: CT HU, no energy spectrum
Crop: 64 x 64 x 64
Train samples: 1000
Validation samples: 128
Epochs: 5
Exported predictions: 64
Generated artifacts
• best.pt checkpoint
• Dose_Bx_CPy.mha predictions
• prediction_manifest.csv
• per-sample metrics CSV
• summary metrics CSV

## Slide 5
Performance Summary
Full-volume exported validation predictions, n = 64
masked relative MAE
13.12%
gamma 3%/3mm
~0.0000007
prediction time
0.112 s/sample
• The pipeline works end-to-end, but model quality is still weak.
• Gamma pass rate is essentially zero, so spatial dose agreement is not clinically useful yet.
• The model still underfits and tends to predict low-amplitude dose.
• Full-image MAE is misleading because most voxels are near zero; masked/high-dose metrics matter more.
Key file: outputs/baseline_hu_no_energy_v2_linear/evaluate_exported/exported_prediction_summary.csv

## Slide 6
Next Steps
Recommended discussion points
• Increase mask_weight to emphasize the dose-support region.
• Add a beam geometry mask/channel as an explicit spatial prior.
• Compare HU vs HU-to-density input.
• Compare no-energy vs with-energy conditioning.
• Try sliding full-volume inference instead of crop insertion.
• Train longer with more samples after the above changes.
Immediate priority
Improve dose-support learning before scaling up expensive training.
Success signal: gamma pass rate and masked relative MAE improve, not only full-volume MAE.